## Slide 1
Do you hear a slow ramp up in motor RPM?
Put Drill in Clutch #1, Speed 3 and pull the trigger, hold for 2 seconds.
When Drill reaches steady speed, is it slower than the top speed for Drill Mode?
When Drill reaches steady speed, do you hear a higher RPM than the steady speed when in Clutch #1, but still slower than Drill Mode?
Put Drill in Clutch #2, Speed 3 and pull the trigger.
Drill is functioning correctly.
YES
Drill is functioning correctly.
YES
NO
NO
A
FUNCTIONAL CHECK:
To better diagnose our new eClutch and related sensors. We have assembled an initial diagnostic flowchart to better pinpoint the root cause of a potential customer complaint.
A customer may come in with a complaint that the drill is drilling in clutch mode or clutching out in drill (or hammer) mode. In either case the following flowchart should be followed to ensure that the drill is functioning correctly before disassembly.
DCD991 / DCD996 eClutch Diagnostic Flowchart [DOC100271506: Rev-0]
NO
YES
Did the tool maintain a steady speed?
C
YES
NO
D
D

## Slide 2
Put Drill in Clutch #11, Speed 3 and pull the trigger.
Do you hear the tool reach steady speed faster than when in clutch #2?
When Drill reaches top speed, do you hear a similar speed as Drill Mode?
Put Drill in DRILL MODE, Speed 3 and pull the trigger.
Drill is functioning correctly.
YES
NO
YES
NO
Drill is functioning correctly.
Is the motor response immediate (e.g. no ramp up) when you pull the trigger?
A
FIRMLY grab chuck wearing leather work gloves and pull trigger.
Put Drill back into Clutch #1, Speed 3.
B
YES
NO
D
D
D

## Slide 3
B
Does Drill clutch out immediately?
Release hand from Chuck. Drill is functioning correctly.
YES
NO
NO
C
Put Drill in Clutch #1, Speed 3 and pull the trigger 10 times for 2 seconds each time.
(Do not hold the chuck.)
Did the unit reach and sustain a top speed 8 out of the 10 times?
Drill is functional.
(Return to top of diagnostics if not already completed)
Replace transmission SA’s #19, #20, and ring gear #16
YES
C
Did you already replace the transmission SA’s?
NO
C
Replace Tool
YES
D

## Slide 4
Is the Ω value within the range given in the table?
While on ESD mat with grounding wrist strap; pull motor out of transmission.
Disconnect Clutch Position Sensor (CPS) from Switch Module. Make sure the pins were seated in the connector and not installed under it.
NO
ELECTRICAL CHECK:
Remove housing and gearcase screws, opening up and removing cover side handle. Carefully remove Transmission Front End and Module/Motor together as one full unit.
Inspect all wires for pinches, nicks, or cuts. Anything abnormal can effect function.
This next step is to interrogate the electrical inputs and outputs from Clutch Position Sensor (CPS)
Put Clutch Collar in Clutch Setting #1
Repeat for all Clutch Settings (#2 to #11), DRILL MODE and HAMMER MODE.
YES
E
D
Clutch Setting | Ω ±1%
#1 | 2000
#2 | 4000
#3 | 5870
#4 | 7740
#5 | 9790
#6 | 12600
#7 | 16400
#8 | 21040
#9 | 27380
#10 | 37140
#11 | 50140
DRILL | 72240
HAMMER | 106240
With multi-meter, probe the 2 pins of the CPS connector.

## Slide 5
Are all wires, and connector pins/bodies in good condition?
Visually inspect Clutch Position Sensor (CPS) wires
Replace Service SA Gear Case
(HD: Item#1-11)
(DD: Item#1, 6-11)
YES
Replace Module
(Item# 34)
NO
YES
Are all wires, connections and connector pins/bodies from module intact?
NO
ELECTRO-MECHANICAL CHECK:
Further disassembly is not required.
Reassemble Front End
E

## Slide 6: Image Appendix

## Slide 7
Ground Wire (BLK)
Power Wire (RED)
LED on indicates power to Sensor

## Slide 8
Connector pins should be pushed fully into connector body.
Occasionally the pins will get bent down and slide under the mating connector instead of into. Inspect units for this, and be sure not to do this.